## Slide 1: Cyber Discovery 2.0
Investigative Session 3
Wireless Networks

## Slide 2: Wired vs. Wireless
Wired networks use wires
Wireless networks use waves at a specific frequency
  Usually 2.4GHz
  Also 5GHz but it's less common

## Slide 3: Wireless Networks
Modulation and demodulation occur at each end
  Modulation: encoding a message in another signal for transport
  Demodulation: the reverse

## Slide 4: Wireless AP
Wireless clients connect to an access point (AP)
  This is a central device (usually a router)

## Slide 5: Wireless AP
APs have an SSID (Service Set Identifier)
Channels separate the 2.4GHz or 5GHz range into bands
  This helps deal with interference
  Other devices also operate at that frequency
Traffic flowing on the network can be encrypted

## Slide 6: Security
In order to compromise the network, we must gain access to the network
This is hard for wired networks
  The attacker must physically connect to the network
  The attacker must be located on the premises
This is made easier on wireless networks
  The AP broadcasts its signal over the air
  The attacker can be inconspicuous

## Slide 7: Security
Several techniques can increase security
  Hiding the SSID
    But this is not always a good thing
  Filtering the MAC address of clients
    We can implement a white list or a black list
  Encrypting the network traffic
    WEP (weaker)
    WPA/WPA2 (stronger)

## Slide 8: WEP
Wired Equivalent Privacy
Uses a 64- or 128-bit key (passphrase)
Key is sent over the network prior to the encrypted data
The same key is used to encrypt every packet

## Slide 9: Cracking WEP
Fairly simple because we can obtain useful information with each packet we sniff
  Remember that the same key is used to encrypt every packet
We can also speed this up using statistical methods
You probably shouldn't use WEP in your own wireless networks because it's trivial to break

## Slide 10: WPA/WPA2
Uses a 128-bit preshared key to associate with the AP
From there, new keys are dynamically created for each session
The key changes often and is only used to encrypt a small number of packets before it changes again
This greatly increases security

## Slide 11: Cracking WPA/WPA2
Can only be done using brute force methods
We typically capture the handshake between a client and the AP when the client associates with the AP
We then iterate through an alphabet or a dictionary to try to determine the passphrase

## Slide 12: Cracking WPA/WPA2
First let's look at how long it takes to discover passphrases using brute force methods
  Suppose the passphrase is 5 characters long and only uses lowercase letters
  Suppose our machine can test 500,000 keys per second
  265 / 500000 = ~30 seconds
  Not too bad, but how realistic is a 5-character passphrase?

## Slide 13: Cracking WPA/WPA2
Now suppose we increase the length to 8 characters
  268 / 500000 = ~5 days
What about 12 characters?
  2612 / 500000 = ~6,000 years!
What about including uppercase letters and digits?
  6212 / 500000 = over 204 million years!

## Slide 14: Cracking WPA/WPA2
Most passphrases are 8 characters and require uppercase, lowercase, and digits
  628 / 500000 = ~14 years
I suggest using all lowercase letters but having a long passphrase (say 15 characters)
  2615 / 500000 = over 106 million years!
  Sing a song...

## Slide 15: Attacks
Wardriving
  Driving around...
Evil twin
  Impersonation of an AP
  Clients automatically connect (usually the default)
  Attackers can sniff and gain information that way
  Also called a “cafe latte” attack

## Slide 16: Warning
Using some of this stuff outside the context of the camp can be unethical and even illegal
Do not try these things on networks that you do not own or maintain (and get permission)
At camp, the only networks you can “play” with are:
  cyberdiscovery
  ?

## Slide 17: Cracking WPA/WPA2
The general process:
  Switch our wireless NIC (Network Interface Card) to monitor traffic without actually associating to any AP
  Capture the handshake
  Crack the preshared key using brute force methods (e.g., with a dictionary)
  There are two dictionaries on your laptop in the “thursday” folder
    words.txt (2,269 words)
    morewords.txt (75,406 words)

## Slide 18: Cracking WPA/WPA2

## Slide 19: Cracking WPA/WPA2
We first run the application wpa-handshake to capture the WPA/WPA2 handshake
We must specify the SSID of the AP we wish to attack
  In our case, the SSID is cyberdiscovery

## Slide 20: Cracking WPA/WPA2

## Slide 21: Cracking WPA/WPA2
At this point we are attempting to capture the handshake
This will not occur unless one or more clients associate with the AP while we're capturing
  We will do this manually by having several clients connect to the network
Eventually, most will capture the handshake
  But this is not always easy nor is it straightforward
  Sometimes it can take a while

## Slide 22: Cracking WPA/WPA2

## Slide 23: Cracking WPA/WPA2

## Slide 24: Cracking WPA/WPA2
Now abort with Ctrl+C
The next step is to run wpa-crack to attempt to discover the preshared key by repeatedly trying words from a dictionary
  We'll use the small dictionary (words.txt) for now
It's important that we specify the MAC address of the AP so that we pick the correct handshakes from the capture file if there are several APs

## Slide 25: Cracking WPA/WPA2

## Slide 26: Cracking WPA/WPA2
The first attempt at cracking the preshared key with the small dictionary is unsuccessful

## Slide 27: Cracking WPA/WPA2

## Slide 28: Cracking WPA/WPA2
So we try again with the larger dictionary (morewords.txt)

## Slide 29: Cracking WPA/WPA2

## Slide 30: Cracking WPA/WPA2
We successfully crack the preshared key and discover it to be “cyberspace”
Note that we would not have been successful if our dictionary did not contain “cyberspace”
  We observed this with the smaller dictionary

## Slide 31: Cracking WPA/WPA2

## Slide 32: Cracking WPA/WPA2
And now we can associate with the AP and gain access to the wireless network
The traffic is now decrypted for us and we can begin to sniff the network traffic